## Slide 1: EE227 – Digital Logic Design
Lecture 19 – 20

## Slide 2: Outline
Flip Flops
D – Flip Flop
JK Flip Flop
T – Flip Flop
Quiz 3 Solution
Code Conversion Combinational Circuit
Quiz 4
Quiz 4 Solution

## Slide 3: Latch and Flip Flop
Latches
  Storage elements that operate with signal levels are referred to as latches
Flip Flops
  Storage elements that are controlled by a clock transition are flip-flops

## Slide 4: SR Latch

## Slide 5: D Latch

## Slide 6: Conversion of D Latch to Flip Flop
The state of a latch or flip-flop is switched by a change in the control input
This momentary change is called a trigger, and the transition it causes is said to trigger the flip-flop
The D latch with pulses in its control input is essentially a flip-flop that is triggered every time the pulse goes to the logic-1 level
As long as the pulse input remains at this level, any changes in the data input will change the output and the state of the latch

## Slide 7: Problem with using Latches in Sequential Circuits (1/2)
In a sequential circuit the inputs of the flip-flops are derived in part from the outputs of the same and other flip-flops
The state transitions of the latches start as soon as the clock pulse changes to the logic-1 level
The new state of a latch appears at the output while the pulse is still active
If the inputs applied to the latches change while the clock pulse is still at the logic-1 level, the latches will respond to new values and a new output state may occur
The result is an unpredictable situation

## Slide 8: Problem with using Latches in Sequential Circuits (2/2)
If the inputs applied to the latches change while the clock pulse is still at the logic-1 level, the latches will respond to new values and a new output state may occur
The result is an unpredictable situation
Because of this unreliable operation, the output of a latch cannot be applied directly or through combinational logic to the input of the same or another latch when all the latches are triggered by a common clock source

## Slide 9: Flip Flops (1/3)
Flip-flop circuits are constructed in such a way as to make them operate properly when they are part of a sequential circuit that employs a common clock
The problem with the latch is that it responds to a change in the level of a clock pulse

## Slide 10: Flip Flops (2/3)
The key to the proper operation of a flip-flop is to trigger it only during a signal transition
A clock pulse goes through two transitions:
  From 0 to 1
    Positive edge transition
  From 1 to 0
    Negative edge transition

## Slide 11: Flip Flops (3/3)
There are two ways that a latch can be modified to form a flip-flop
  One way is to employ two latches in a special configuration that isolates the output of the flip-flop and prevents it from being affected while the input to the flip-flop is changing
  Another way is to produce a flip-flop that triggers only during a signal transition (from 0 to 1 or from 1 to 0) of the synchronizing signal (clock) and is disabled during the rest of the clock pulse

## Slide 12: Edge Triggered D – Flip Flop with D Latches
Master – Slave Configuration
A change in the output of the flip-flop can be triggered only by and during the transition of the clock from 1 to 0

## Slide 13: Edge Triggered D – Flip Flop with SR Latches
When Clk = 0
  R = 1, S = 1
  No change in state
When D = 0 and Clk changes from 0 to 1
  R = 0, S = 1  Q = 0
  Reset state
  Further change in D when Clk = 1
  Locked state as R = 0
When D = 1 and Clk changes from 0 to 1
  S = 0, R = 1  Q = 1
  Set State

## Slide 14: Setup, Hold and Propagation Delay Time
There is a minimum time called the setup time during which the D input must be maintained at a constant value prior to the occurrence of the clock transition
There is a minimum time called the hold time during which the D input must not change after the application of the positive transition of the clock
The propagation delay time of the flip-flop is defined as the interval between the trigger edge and the stabilization of the output to a new state

## Slide 15: Graphical Symbols of D – Flip Flop
The dynamic indicator (>) denotes the fact that the flip-flop responds to the edge transition of the clock

## Slide 16: Other Flip Flops
There are three operations that can be performed with a flip-flop
  Set it to 1
  Reset it to 0
  Complement its output
With only a single input, the D flip-flop can set or reset the output
There are two other flip flops
  JK flip flop
  T flip flop

## Slide 17: JK Flip Flop
2 inputs J and K
Performs all 3 operations
D = JQ’ + K’Q

## Slide 18: Toggle (T) – Flip Flop
The T (toggle) flip-flop is a complementing flip-flop and can be obtained from a JK flip-flop when inputs J and K are tied together
The T flip-flop can be constructed with a D flip-flop and an exclusive-OR gate as
D = T  Q = TQ’ + T’Q

## Slide 19: Characteristic Equations
The next state [Q(t + 1)] can be obtained with the help of characteristic equations
For D – Flip Flop
Q(t + 1) = D
For JK Flip Flop
Q(t + 1) = JQ’ + K’Q
For T – Flip Flop
Q(t + 1) = T  Q = TQ’ + T’Q

## Slide 20: Direct Inputs in Flip Flops
Some flip-flops have asynchronous inputs that are used to force the flip-flop to a particular state independently of the clock
The input that sets the flip-flop to 1 is called preset or direct set
The input that clears the flip-flop to 0 is called clear or direct reset

## Slide 21: Edge Triggered D Flip Flop with Direct Reset

## Slide 22: Code Conversion Combinational Circuit
Missed Topic from Chapter 4

## Slide 23: BCD to Excess – 3 Code Conversion (1/4)
Truth Table

## Slide 24: BCD to Excess – 3 Code Conversion (2/4)
K – Map Simplification

## Slide 25: BCD to Excess – 3 Code Conversion (3/4)
Boolean Equations
  z = D’
  y = CD + C’D’
  y = CD + (C + D)’
  x = B’C + B’D + BC’D’
  x = B’(C + D) + BC’D’
  x = B’(C + D) + B(C + D)’
  w = A + BC + BD
  w = A + B(C + D)

## Slide 26: BCD to Excess – 3 Code Conversion (4/4)
Circuit Diagram

## Slide 27: Quiz 3 and 4
Solution
Was Done in Class