## Slide 2: Sequential Circuits
Combinational
Circuit
Memory Elements
Inputs
Outputs
Asynchronous
Synchronous
Combinational
Circuit
Flip-flops
Inputs
Outputs
Clock

## Slide 3: Latches
SR Latch
S R Q0 | Q | Q’
0 0 0 |  | 
0
1
0
0
0 | 1
Q = Q0
Initial Value

## Slide 4: Latches
SR Latch
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 |  | 
1
0
0
0
1 | 0
Q = Q0
Q = Q0

## Slide 5: Latches
SR Latch
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 
0
1
1
0
 | 1
Q = 0
Q = Q0

## Slide 6: Latches
SR Latch
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 |  | 
1
0
1
0
0 | 1
Q = 0
Q = Q0
Q = 0

## Slide 7: Latches
SR Latch
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1 0 0 |  | 
0
1
0
1
1 | 0
Q = 0
Q = Q0
Q = 1

## Slide 8: Latches
SR Latch
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1 0 0 | 1 | 0
1 0 1 |  | 
1
0
0
1
1 | 0
Q = 0
Q = Q0
Q = 1
Q = 1

## Slide 9: Latches
SR Latch
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1 0 0 | 1 | 0
1 0 1 | 1 | 0
1 1 0 |  | 
0
1
1
1
0 | 0
Q = 0
Q = Q0
Q = 1
Q = Q’
0

## Slide 10: Latches
SR Latch
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1 0 0 | 1 | 0
1 0 1 | 1 | 0
1 1 0 | 0 | 0
1 1 1 |  | 
1
0
1
1
0 | 0
Q = 0
Q = Q0
Q = 1
Q = Q’
0
Q = Q’

## Slide 11: Latches
SR Latch
S R | Q
0 0 | Q0
0 1 | 0
1 0 | 1
1 1 | Q=Q’=0
No change
Reset
Set
Invalid
S R | Q
0 0 | Q=Q’=1
0 1 | 1
1 0 | 0
1 1 | Q0
Invalid
Set
Reset
No change

## Slide 12: Latches
SR Latch
S R | Q
0 0 | Q0
0 1 | 0
1 0 | 1
1 1 | Q=Q’=0
No change
Reset
Set
Invalid
S’ R’ | Q
0 0 | Q=Q’=1
0 1 | 1
1 0 | 0
1 1 | Q0
Invalid
Set
Reset
No change

## Slide 13: Controlled Latches
SR Latch with Control Input
C S R | Q
0 x x | Q0
1 0 0 | Q0
1 0 1 | 0
1 1 0 | 1
1 1 1 | Q=Q’
No change
No change
Reset
Set
Invalid

## Slide 14: Controlled Latches
D Latch (D = Data)
C D | Q
0 x | Q0
1 0 | 0
1 1 | 1
No change
Reset
Set
C
Timing Diagram
D
Q
t
Output may change

## Slide 15: Controlled Latches
D Latch (D = Data)
C D | Q
0 x | Q0
1 0 | 0
1 1 | 1
No change
Reset
Set
C
Timing Diagram
D
Q
Output may change

## Slide 16: Flip-Flops
Controlled latches are level-triggered
Flip-Flops are edge-triggered
C
CLK
Positive Edge
CLK
Negative Edge

## Slide 17: Issue with latch

## Slide 18
Note that the problem with the latch is that it is transparent: As soon as an input changes, shortly thereafter the corresponding output changes to match it. This transparency is what allows a change on a latch output to produce additional changes at other latch outputs while the clock pulse is at logic 1. The key to the proper operation of flip-flops is to prevent them from being transparent. In a flipflop, before an output can change, the path from its inputs to its outputs is broken. So, a flip-flop cannot “see” the change of its output or of the outputs of other, similar flip-flops at its input during the same clock pulse. Thus, the new state of a flip-flop depends only on the immediately preceding state, and the flip-flops do not go through multiple changes of state. There are two ways that latches are combined to form a flip-flop. One way is to combine two latches such that (1) the inputs presented to the flip-flop when a clock pulse is present control its state and (2) the state of the flip-flop changes only when a clock pulse is not present. Such a circuit is called a master–slave flipflop. Another way is to produce a flip-flop that triggers only during a signal transition from 0 to 1 (or from 1 to 0) on the clock and that is disabled at all other times, including for the duration of the clock pulse. Such a circuit is said to be an edge-triggered flip-flop.

## Slide 19: 1s catching problem

## Slide 20: Flip-Flops
Master-Slave D Flip-Flop
D Latch
(Master)
D
C
Q
D Latch
(Slave)
D
C
Q
Q
D
CLK
CLK
D
QMaster
QSlave
Looks like it is negative edge-triggered
Master
Slave

## Slide 21: EDGE TRIGGERING OF D FLIP FLOP

## Slide 22: Flip-Flops
Edge-Triggered D Flip-Flop
D
Q
Q
D
Q
Q
Positive Edge
Negative Edge
Notes: CP
D
R
S
Q(t+1)
0
0
1
1
PS
0
1
1
1
PS
1
0
1
0
0 reset
1
1
1
0
0
0
X
1
1
PS
1
1
0
1
1set

## Slide 23: Edge-Triggered D Flip-Flop
CP | D | S | R | Q(t+1)
0 | 0 | 1 | 1 | PS
0 | 1 | 1 | 1 | PS
1 | 0 | 1 | 0 | 0Reset
1 | 1 | 1 | 0 | 0
0 | X | 1 | 1 | PS
1 | 1 | 0 | 1 | 1set
1 | 0 | 0 | 1 | 1set

## Slide 24: Flip-Flops
JK Flip-Flop
J
Q
Q
K
D = JQ’ + K’Q

## Slide 25: Flip-Flops
T Flip-Flop
D = TQ’ + T’Q = T  Q
J
Q
Q
K
T
D
Q
Q
T
D = JQ’ + K’Q
T
Q
Q

## Slide 26: Flip-Flop Characteristic Tables
D
Q
Q
D | Q(t+1)
0 | 0
1 | 1
Reset
Set
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q’(t)
No change
Reset
Set
Toggle
J
Q
Q
K
T
Q
Q
T | Q(t+1)
0 | Q(t)
1 | Q’(t)
No change
Toggle

## Slide 27: Flip-Flop Characteristic Equations
D
Q
Q
D | Q(t+1)
0 | 0
1 | 1
Q(t+1) = D
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q’(t)
Q(t+1) = JQ’ + K’Q
J
Q
Q
K
T
Q
Q
T | Q(t+1)
0 | Q(t)
1 | Q’(t)
Q(t+1) = T  Q

## Slide 28: Flip-Flop Characteristic Equations
Analysis / Derivation
J
Q
Q
K
J | K | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
No change
Reset
Set
Toggle

## Slide 29: Flip-Flop Characteristic Equations
Analysis / Derivation
J
Q
Q
K
J | K | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
No change
Reset
Set
Toggle

## Slide 30: Flip-Flop Characteristic Equations
Analysis / Derivation
J
Q
Q
K
J | K | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 
1 | 1 | 1 | 
No change
Reset
Set
Toggle

## Slide 31: Flip-Flop Characteristic Equations
Analysis / Derivation
J
Q
Q
K
J | K | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
No change
Reset
Set
Toggle

## Slide 32: Flip-Flop Characteristic Equations
Analysis / Derivation
J
Q
Q
K
J | K | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
 |  |  |  | K | 
 |  | 0 | 1 | 0 | 0
J |  | 1 | 1 | 0 | 1
 |  |  | Q |  | 
Q(t+1) = JQ’ + K’Q

## Slide 33: Flip-Flops with Direct Inputs
Asynchronous Reset
D
Q
Q
R
Reset
R’ | D | CLK | Q(t+1)
0 | x | x | 0

## Slide 34: Flip-Flops with Direct Inputs
Asynchronous Reset
D
Q
Q
R
Reset
R’ | D | CLK | Q(t+1)
0 | x | x | 0
1 | 0 | ↑ | 0
1 | 1 | ↑ | 1

## Slide 35: Flip-Flops with Direct Inputs
Asynchronous Preset and Clear
PR’ | CLR’ | D | CLK | Q(t+1)
1 | 0 | x | x | 0
D
Q
Q
CLR
Reset
PR
Preset

## Slide 36: Flip-Flops with Direct Inputs
Asynchronous Preset and Clear
PR’ | CLR’ | D | CLK | Q(t+1)
1 | 0 | x | x | 0
0 | 1 | x | x | 1
D
Q
Q
CLR
Reset
PR
Preset

## Slide 37: Flip-Flops with Direct Inputs
Asynchronous Preset and Clear
PR’ | CLR’ | D | CLK | Q(t+1)
1 | 0 | x | x | 0
0 | 1 | x | x | 1
1 | 1 | 0 | ↑ | 0
1 | 1 | 1 | ↑ | 1
D
Q
Q
CLR
Reset
PR
Preset

## Slide 38: Analysis of Clocked Sequential Circuits
The State
  State = Values of all Flip-Flops
Example
A B = 0 0

## Slide 39: Analysis of Clocked Sequential Circuits
State Equations
A(t+1) = DA
= A(t) x(t)+B(t) x(t)
= A x + B x
B(t+1) = DB
= A’(t) x(t)
= A’ x
y(t) = [A(t)+ B(t)] x’(t)
= (A + B) x’

## Slide 40: Analysis of Clocked Sequential Circuits
State Table (Transition Table)
A(t+1) = A x + B x
B(t+1) = A’ x
y(t) = (A + B) x’
Present State |  | Input | Next State |  | Output
A | B | x | A | B | y
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 
t+1
t
t
0 0 0
0 1 0
0 0 1
1 1 0
0 0 1
1 0 0
0 0 1
1 0 0

## Slide 41: Analysis of Clocked Sequential Circuits
State Table (Transition Table)
A(t+1) = A x + B x
B(t+1) = A’ x
y(t) = (A + B) x’
Present State |  |  | Next State |  |  |  | Output | 
 |  |  | x = 0 |  | x = 1 |  | x = 0 | x = 1
A |  | B | A | B | A | B | y | y
0 |  | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 |  | 1 | 0 | 0 | 1 | 1 | 1 | 0
1 |  | 0 | 0 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 0 | 0 | 1 | 0 | 1 | 0
t+1
t
t

## Slide 42: Analysis of Clocked Sequential Circuits
State Diagram
0 0
1 0
0 1
1 1
0/0
0/1
1/0
1/0
1/0
1/0
0/1
0/1
AB
input/output
Present State |  |  | Next State |  |  |  | Output | 
 |  |  | x = 0 |  | x = 1 |  | x = 0 | x = 1
A |  | B | A | B | A | B | y | y
0 |  | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 |  | 1 | 0 | 0 | 1 | 1 | 1 | 0
1 |  | 0 | 0 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 0 | 0 | 1 | 0 | 1 | 0

## Slide 43: Analysis of Clocked Sequential Circuits
D Flip-Flops
Example:
D
Q
Q
x
CLK
y
A
Present State | Input |  | Next State
A | x | y | A
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
0
1
1
0
1
0
0
1
0
1
00,11
00,11
01,10
01,10
A(t+1) = DA = A  x  y

## Slide 44: Analysis of Clocked Sequential Circuits
JK Flip-Flops
Example:
JA = B KA = B x’
JB = x’ KB = A  x
A(t+1) = JA Q’A + K’A QA
= A’B + AB’ + Ax
B(t+1) = JB Q’B + K’B QB
= B’x’ + ABx + A’Bx’
Present State |  | I/P | Next State |  | Flip-Flop Inputs |  |  | 
A | B | x | A | B | JA | KA | JB | KB
0 | 0 | 0 |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  | 
0 0 1 0
0 0 0 1
1 1 1 0
1 0 0 1
0 0 1 1
0 0 0 0
1 1 1 1
1 0 0 0
0 1
0 0
1 1
1 0
1 1
1 0
0 0
1 1

## Slide 45: Analysis of Clocked Sequential Circuits
JK Flip-Flops
Example:
Present State |  | I/P | Next State |  | Flip-Flop Inputs |  |  | 
A | B | x | A | B | JA | KA | JB | KB
0 | 0 | 0 |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  | 
0 0 1 0
0 0 0 1
1 1 1 0
1 0 0 1
0 0 1 1
0 0 0 0
1 1 1 1
1 0 0 0
0 1
0 0
1 1
1 0
1 1
1 0
0 0
1 1
0 0
1 1
0 1
1 0
1
0
1
0
1
0
0
1

## Slide 46: Analysis of Clocked Sequential Circuits
T Flip-Flops
Example:
TA = B x TB = x
y = A B
A(t+1) = TA Q’A + T’A QA
= AB’ + Ax’ + A’Bx
B(t+1) = TB Q’B + T’B QB
= x  B
Present State |  | I/P | Next State |  | F.F Inputs |  | O/P
A | B | x | A | B | TA | TB | y
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 
0 0
0 1
0 0
1 1
0 0
0 1
0 0
1 1
0 0
0 1
0 1
1 0
1 0
1 1
1 1
0 0
0
0
0
0
0
0
1
1

## Slide 47: Analysis of Clocked Sequential Circuits
T Flip-Flops
Example:
Present State |  | I/P | Next State |  | F.F Inputs |  | O/P
A | B | x | A | B | TA | TB | y
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 
0 0
0 1
0 0
1 1
0 0
0 1
0 0
1 1
0 0
0 1
0 1
1 0
1 0
1 1
1 1
0 0
0
0
0
0
0
0
1
1
0 0
0 1
1 1
1 0
0/0
1/0
0/0
1/0
1/0
1/1
0/0
0/1

## Slide 48: Mealy and Moore Models
The Mealy model: the outputs are functions of both the present state and inputs (Fig. 5-15).
  The outputs may change if the inputs change during the clock pulse period.
    The outputs may have momentary false values unless the inputs are synchronized with the clocks.
The Moore model: the outputs are functions of the present state only (Fig. 5-20).
  The outputs are synchronous with the clocks.

## Slide 49: Mealy and Moore Models
Fig. 5.21 Block diagram of Mealy and Moore state machine

## Slide 50: Mealy and Moore Models
Present State |  | I/P | Next State |  | O/P
A | B | x | A | B | y
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0
Mealy
For the same state, the output changes with the input
Present State |  | I/P | Next State |  | O/P
A | B | x | A | B | y
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1
Moore
For the same state, the output does not change with the input

## Slide 51: Moore State Diagram
State / Output
0 0 / 0
0 1 / 0
1 1 / 1
1 0 / 0
0
1
1
1
0
0
0
1

## Slide 52: State Reduction and Assignment
State Reduction Reductions on the number of flip-flops and the number of gates.
  A reduction in the number of states may result in a reduction in the number of flip-flops.
  An example state diagram showing in Fig. 5.25.
Fig. 5.25 State diagram

## Slide 53: State Reduction
  Only the input-output sequences are important.
  Two circuits are equivalent
    Have identical outputs for all input sequences;
    The number of states is not important.
Fig. 5.25 State diagram
State: | a | a | b | c | d | e | f | f | g | f | g | a
Input: | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 
Output: | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 

## Slide 54
Equivalent states
  Two states are said to be equivalent
    For each member of the set of inputs, they give exactly the same output and send the circuit to the same state or to an equivalent state.
    One of them can be removed.

## Slide 55
Reducing the state table
  e = g (remove g);
  d = f (remove f);

## Slide 56
  The reduced finite state machine
State: | a | a | b | c | d | e | d | d | e | d | e | a
Input: | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 
Output: | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 

## Slide 57
  The checking of each pair of states for possible equivalence can be done systematically using Implication Table.
  The unused states are treated as don't-care condition Þ fewer combinational gates.
Fig. 5.26 Reduced State diagram

## Slide 58: Implication Table
The state-reduction procedure for completely specified state tables is based on the algorithm that two states in a state table can be combined into one if they can be shown to be equivalent. There are occasions when a pair of states do not have the same next states, but, nonetheless, go to equivalent next states. Consider the following state table:
(a, b) imply (c, d) and (c, d) imply (a, b). Both pairs of states are equivalent; i.e., a and b are equivalent as well as c and d.

## Slide 59: Implication Table
The checking of each pair of states for possible equivalence in a table with a large number of states can be done systematically by means of an implication table. This a chart that consists of squares, one for every possible pair of states, that provide spaces for listing any possible implied states. Consider the following state table:

## Slide 60: Implication Table
The implication table is:

## Slide 61: Implication Table
On the left side along the vertical are listed all the states defined in the state table except the last, and across the bottom horizontally are listed all the states except the last.
The states that are not equivalent are marked with a ‘x’ in the corresponding square, whereas their equivalence is recorded with a ‘√’.
Some of the squares have entries of implied states that must be further investigated to determine whether they are equivalent or not.
The step-by-step procedure of filling in the squares is as follows:
  Place a cross in any square corresponding to a pair of states whose outputs are not equal for every input.
  Enter in the remaining squares the pairs of states that are implied by the pair of states representing the squares. We do that by starting from the top square in the left column and going down and then proceeding with the next column to the right.

## Slide 62: Implication Table
  3. Make successive passes through the table to determine whether any additional squares should be marked with a ‘x’. A square in the table is crossed out if it contains at least one implied pair that is not equivalent.
  4. Finally, all the squares that have no crosses are recorded with check marks. The equivalent states are: (a, b), (d, e), (d, g), (e, g).
  We now combine pairs of states into larger groups of equivalent states. The last three pairs can be combined into a set of three equivalent states (d, e,g) because each one of the states in the group is equivalent to the other two. The final partition of these states consists of the equivalent states found from the implication table, together with all the remaining states in the state table that are not equivalent to any other state:
  (a, b) (c) (d, e, g) (f)
  The reduced state table is:

## Slide 63: Implication Table

## Slide 64: State Assignment
State Assignment
To minimize the cost of the combinational circuits.
  Three possible binary state assignments. (m states need n-bits, where 2n > m)

## Slide 65
  Any binary number assignment is satisfactory as long as each state is assigned a unique number.
  Use binary assignment 1.

## Slide 66: Design Procedure
Design Procedure for sequential circuit
  The word description of the circuit behavior to get a state diagram;
  State reduction if necessary;
  Assign binary values to the states;
  Obtain the binary-coded state table;
  Choose the type of flip-flops;
  Derive the simplified flip-flop input equations and output equations;
  Draw the logic diagram;

## Slide 67: Design of Clocked Sequential Circuits
Example:
Detect 3 or more consecutive 1’s
S0 / 0
S1 / 0
S3 / 1
S2 / 0
0
1
1
0
0
1
0
1
State | A B
S0 | 0 0
S1 | 0 1
S2 | 1 0
S3 | 1 1

## Slide 68: Design of Clocked Sequential Circuits
Example:
Detect 3 or more consecutive 1’s
Present State |  | Input | Next State |  | Output
A | B | x | A | B | y
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 
0 0 0
0 1 0
0 0 0
1 0 0
0 0 0
1 1 0
0 0 1
1 1 1
S0 / 0
S1 / 0
S3 / 1
S2 / 0
0
1
1
0
0
1
0
1

## Slide 69: Design of Clocked Sequential Circuits
Example:
Detect 3 or more consecutive 1’s
Present State |  | Input | Next State |  | Output
A | B | x | A | B | y
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 
0 0 0
0 1 0
0 0 0
1 0 0
0 0 0
1 1 0
0 0 1
1 1 1
A(t+1) = DA (A, B, x)
= ∑ (3, 5, 7)
B(t+1) = DB (A, B, x)
= ∑ (1, 5, 7)
y (A, B, x) = ∑ (6, 7)
Synthesis using D Flip-Flops

## Slide 70: Design of Clocked Sequential Circuits with D F.F.
Example:
Detect 3 or more consecutive 1’s
DA (A, B, x) = ∑ (3, 5, 7)
= A x + B x
DB (A, B, x) = ∑ (1, 5, 7)
= A x + B’ x
y (A, B, x) = ∑ (6, 7)
= A B
Synthesis using D Flip-Flops
 |  |  |  | B | 
 |  | 0 | 0 | 1 | 0
A |  | 0 | 1 | 1 | 0
 |  |  | x |  | 
 |  |  |  | B | 
 |  | 0 | 1 | 0 | 0
A |  | 0 | 1 | 1 | 0
 |  |  | x |  | 
 |  |  |  | B | 
 |  | 0 | 0 | 0 | 0
A |  | 0 | 0 | 1 | 1
 |  |  | x |  | 

## Slide 71: Design of Clocked Sequential Circuits with D F.F.
Example:
Detect 3 or more consecutive 1’s
DA = A x + B x
DB = A x + B’ x
y = A B
Synthesis using D Flip-Flops

## Slide 72: Flip-Flop Excitation Tables
Present State | Next State | F.F. Input
Q(t) | Q(t+1) | D
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Present State | Next State | F.F. Input | 
Q(t) | Q(t+1) | J | K
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
0 0 (No change)
0 1 (Reset)
0 x
1 x
x 1
x 0
0
1
0
1
1 0 (Set)
1 1 (Toggle)
0 1 (Reset)
1 1 (Toggle)
0 0 (No change)
1 0 (Set)
Q(t) | Q(t+1) | T
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
1
1
0

## Slide 73: Design of Clocked Sequential Circuits with JK F.F.
Example:
Detect 3 or more consecutive 1’s
Present State |  | Input | Next State |  | Flip-Flop Inputs |  |  | 
A | B | x | A | B | JA | KA | JB | KB
0 | 0 | 0 | 0 | 0 |  |  |  | 
0 | 0 | 1 | 0 | 1 |  |  |  | 
0 | 1 | 0 | 0 | 0 |  |  |  | 
0 | 1 | 1 | 1 | 0 |  |  |  | 
1 | 0 | 0 | 0 | 0 |  |  |  | 
1 | 0 | 1 | 1 | 1 |  |  |  | 
1 | 1 | 0 | 0 | 0 |  |  |  | 
1 | 1 | 1 | 1 | 1 |  |  |  | 
0 x
0 x
0 x
1 x
x 1
x 0
x 1
x 0
JA (A, B, x) = ∑ (3)
dJA (A, B, x) = ∑ (4,5,6,7)
KA (A, B, x) = ∑ (4, 6)
dKA (A, B, x) = ∑ (0,1,2,3)
JB (A, B, x) = ∑ (1, 5)
dJB (A, B, x) = ∑ (2,3,6,7)
KB (A, B, x) = ∑ (2, 3, 6)
dKB (A, B, x) = ∑ (0,1,4,5)
Synthesis using JK F.F.
0 x
1 x
x 1
x 1
0 x
1 x
x 1
x 0

## Slide 74: Design of Clocked Sequential Circuits with JK F.F.
Example:
Detect 3 or more consecutive 1’s
JA = B x KA = x’
JB = x KB = A’ + x’
Synthesis using JK Flip-Flops
 |  |  |  | B | 
 |  | 0 | 0 | 1 | 0
A |  | x | x | x | x
 |  |  | x |  | 
 |  |  |  | B | 
 |  | x | x | x | x
A |  | 1 | 0 | 0 | 1
 |  |  | x |  | 
 |  |  |  | B | 
 |  | 0 | 1 | x | x
A |  | 0 | 1 | x | x
 |  |  | x |  | 
 |  |  |  | B | 
 |  | x | x | 1 | 1
A |  | x | x | 0 | 1
 |  |  | x |  | 

## Slide 75: Design of Clocked Sequential Circuits with T F.F.
Example:
Detect 3 or more consecutive 1’s
Present State |  | Input | Next State |  | F.F. Input
A | B | x | A | B | TA TB
0 | 0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 1 | 
0 | 1 | 0 | 0 | 0 | 
0 | 1 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 0 | 
1 | 0 | 1 | 1 | 1 | 
1 | 1 | 0 | 0 | 0 | 
1 | 1 | 1 | 1 | 1 | 
0
0
0
1
1
0
1
0
Synthesis using T Flip-Flops
0
1
1
1
0
1
1
0
TA (A, B, x) = ∑ (3, 4, 6)
TB (A, B, x) = ∑ (1, 2, 3, 5, 6)

## Slide 76: Design of Clocked Sequential Circuits with T F.F.
Example:
Detect 3 or more consecutive 1’s
TA = A x’ + A’ B x
TB = A’ B + B  x
Synthesis using T Flip-Flops
 |  |  |  | B | 
 |  | 0 | 0 | 1 | 0
A |  | 1 | 0 | 0 | 1
 |  |  | x |  | 
 |  |  |  | B | 
 |  | 0 | 1 | 1 | 1
A |  | 0 | 1 | 0 | 1
 |  |  | x |  |