## Slide 1: EE227 – Digital Logic Design
Lecture 26

## Slide 2: Outline
Ripple Counters
  Binary Ripple Counter
  BCD Ripple Counter
Synchronous Counter
  Binary Counter
  Binary Up/Down Counter

## Slide 3: Counters
A register that goes through a prescribed sequence of states upon the application of input pulses is called a counter
Counters are available in two categories
Ripple counters
  In a ripple counter, a flip‐flop output transition serves as a source for triggering other flip‐flops
  Clock is not common
Synchronous counters
  In a synchronous counter, the C inputs of all flip‐flops receive the common clock

## Slide 4: Ripple Counters
In a ripple counter, a flip‐flop output transition serves as a source for triggering other flip‐flops
Clock is not common
We will discuss two types of ripple counters
Binary Ripple Counter
  A counter that follows the binary number sequence (0, 1, 2, 3, …)
BCD Ripple Counter
  A BCD counter follows a sequence of 10 states and returns to 0 after the count of 9

## Slide 5: 4 – Bit Binary Ripple Counter (1/2)
4 bits  4 flip flops are required
LSB (A0) is complementing every time
  Connect the flip flop producing A0 directly to a clock
A1 is changing when A0 changes from 1 to 0 (at negative edge)
  A0 is connected to the clock of flip flop producing A1
A2 is changing when A1 changes from 1 to 0 (at negative edge)
  A1 is connected to the clock of flip flop producing A2
A3 is changing when A2 changes from 1 to 0 (at negative edge)
  A2 is connected to the clock of flip flop producing A3

## Slide 6: 4 – Bit Binary Ripple Counter (2/2)

## Slide 7: BCD Ripple Counter (1/3)
  A BCD counter follows a sequence of 10 states and returns to 0 after the count of 9
10 states  at least 4 flip flops are required
State diagram is shown below

## Slide 8: BCD Ripple Counter (2/3)
Q1 is complemented on every clock pulse
Q2 is complemented if Q8 = 0 and Q1 goes from 1 to 0
Q2 is clear if Q8 = 1 and Q1 goes from 1 to 0
Q4 is complemented if Q2 goes from 1 to 0
Q8 is complemented Q1 goes from 1 to 0
Q8 is cleared if either Q4 or Q2 is 0 and Q1 goes from 1 to 0

## Slide 9: BCD Ripple Counter (3/3)

## Slide 10: BCD Decade Counter
The BCD counter discussed previously is a decade counter as it counts from 0 to 9
To count in decimal from 0 to 99, we need a two‐decade counter
To count from 0 to 999, we need a three‐decade counter
Multiple decade counters can be constructed by connecting BCD counters in cascade, one for each decade

## Slide 11: Synchronous Counters
Synchronous counters are different from ripple counters in that clock pulses are applied to the inputs of all flip‐flops
A common clock triggers all flip‐flops simultaneously, rather than one at a time in succession as in a ripple counter
The design procedure for synchronous counters was presented in chapter 5, and the design of a three‐bit binary counter was carried out
Here we will enhance the design for 4 bit binary counter

## Slide 12: 4 – Bit Synchronous Binary Up Counter

## Slide 13: 4 – Bit Synchronous Binary Up Counter

## Slide 14: 4 – Bit Synchronous Binary Down Counter
From State Table, we get
  TD = A’B’C’
  TC = A’B’
  TB = A’
  TA = 1

## Slide 15: 4 – Bit Synchronous Binary Down Counter

## Slide 16: 3 Bit Binary Up/Down Counter (1/2)
By using K – Map
We Get
TA = 1
TB = M’QA + MQ’A
TC = M’QBQA + MQ’BQ’A

## Slide 17: 4 Bit Binary Up/Down Counter